## Slide 1: Linux SPI Device Driver
BenTsai
2015/10/14

## Slide 2: OUTLINE
I2C
  UART
  Uart Packet Frame
  8250/16450/16550
Linux Device Driver – I2C
  TTY Device/Driver
  Platform Device/Driver
  Uart Driver – 8250 Driver
Adapter : L6021
  Device Tree
Client Device : F75111R
SMBus

## Slide 3: I2C

## Slide 4: I2C 硬體架構
vcc
上拉電阻
上拉電阻
SDA
SCL
I2C 總線
SDA
SCL
SDA
SCL
SDA
SCL

## Slide 5: I2C Data Format
Start Bit : 1 bit, always low.
Data Bit : 5~8 Bit
Parity Bit : None/Even/Odd, three options.
Stop Bit : 1/1.5/2 Bit, always high.
常用設定 : N81, baud rate : 115200.

## Slide 6: I2C Data Format
Start Bit : 1 bit, always low.
Data Bit : 5~8 Bit
Parity Bit : None/Even/Odd, three options.
Stop Bit : 1/1.5/2 Bit, always high.
常用設定 : N81, baud rate : 115200.

## Slide 7: Linux Device Driver – SPI

## Slide 8: Linux - I2C
i2c-core
i2c-adapter
i2c-algorithm
i2c-client (F75111R)
應用程式
/sys,/dev
用戶模式驅動
i2c-core
i2c-dev
i2c-adapter
/algorithm
i2c-adapter
/algorithm
i2c-adapter
/algorithm
i2c-adapter
/algorithm
i2c-client
i2c-client
i2c-client
i2c-client
i2c host controller
i2c slave device
user space
kernel space
HW
Notes: User Space 若要使用Uart, 需要藉由ttyS這個node. 而這個node, 是tty core 向linux kernel 註冊ttys的char device.
藉由tty 的介面與行為, 實際操作Uart.

## Slide 9: SPI驅動框架-master
platform device : SPI
master
board info
client device
platform driver : SPI
client driver
device tree
host controller
slave device
SPI client dts
SPI dts
SPI bus
of_register_spi_devices
spi_add_driver
spi_register_master
of_register_spi_devices
spi_match_master_to_boardinfo
device tree (platform device)
SOCLE_SPI_driver
of_match_table
name
compatible(dts)
name
spi_register_master
spi_match_master_to_boardinfo
(bus_num)
Slave driver
of_match_table
id_table | name
Slave device(dts)
compatible
Slave device
modalias
platforn bus

## Slide 10: L6021 – I2C

## Slide 11: I2C
Feature
  Item Compatible with I2C-bus
  AMBA APB slave interface
  Supports master and slave modes of I2C bus
  Multi master operation
  SW programmable clock frequency and transfer rate up to 400Kbit/sec
  Supports 7 bits and 10 bits addressing modes
  Interrupt or polling driven byte-by-byte data transfer
  Clock stretching and wait state generation

## Slide 12: Master Mode Programming
SCL Clock
Data Receiver Register Access
Start Command and 1’st Byte Address
Interrupt and Resume
Read/Write Command
Multi-Master Arbitration
Master Interrupt Condition
Stop Command

## Slide 13: Detail Register Description
socle_i2c_read_bytes()
socle_i2c_send_bytes()
socle_i2c_do_address()
socle_i2c_stop()

## Slide 15: F75111R

## Slide 16
Notes: http://wiki.csie.ncku.edu.tw/embedded/I2C

## Slide 18
Back Up

## Slide 19: I2C
i2c_regs – Control and Status Registers
The i2c_regs component is used to control the I2C controller operation by the host with APB interface. It implements the register set and the interrupt functionality. The CSR component operates synchronously with the pclk clock.
i2c_master – I2C Master Control and State Machine
The I2C master controller implements the I2C master operation for transmit data to and receive data from other I2C devices. The I2C master controller operates synchronously with the pclk.
i2c_slave – I2C Slave Control and State Machine
The I2C slave controller implements the I2C master operation for transmit data to and receive data from other I2C devices. The I2C slave controller operates synchronously with the pclk.
i2c_divider – Clock Divider
  The clock divider module generates I2C clock SCL output signals from pclk at
  frequency according the given equation.
i2c_interface – I2C interface (These are logics under top module. There is actually no such a module)
  SDA output enable from I2C master controller and slave controller are ANDed together as the output ports. Similarly, SCL output enable from I2C
  master controller and slave controller are ANDed together. SDA output and SCL output are actually ties to the ground since I2C is an open drain
  architecture. So once enabled, SDA/ SCL on I2C will be pulled low.

## Slide 20: Registers Summary

## Slide 21: Detail Register Description

## Slide 22: Detail Register Description

## Slide 23: Detail Register Description

## Slide 24: Detail Register Description

## Slide 25: Detail Register Description

## Slide 26: Detail Register Description

## Slide 27: Detail Register Description

## Slide 28: Detail Register Description